## Slide 1
DEVELOPMENT AND ANALYSIS OF PNEUMATIC CONVEYER.
By
MEGANATHAN M (113221081043)
RISHI V (113221081055)
RITHISH B (113221081056)
THIYAKA VISHNU P (113221081077)
Under the guidance of
MR.LOGANATHAN D
Professor
Department of Mechanical Engineering
Velammal Engineering College
21ME405P - Project Work Phase I
Final Review Presentation
VELAMMAL ENGINEERING COLLEGE
DEPARTMENT OF MECHANICAL ENGINEERING

## Slide 2: PROBLEM IDENTIFICATION
PROBLEMS IN THE POWER TRANSMISSION SYSTEM.
In traditional conveyor systems there are more moving parts and the power transmission system produces fricfricfriction.Due to this friction
1.Damage to goods.
2.Damage to the conveyor system.
3.More power consumption.
4.More maintenance needed.
5.Chance of accidents.

## Slide 3: OBJECTIVE OF THE PROJECT
The objective of this project is to reduce the moving parts and make a new type of conveyor system with the help of air pressure created by blower. At the end of the project these objectives are reached.
1.To ensure the Smooth movement of goods.
2.To make Frictionless movement.
3.To reduce the Power consumption and increase
efficiency.
4.To reduce the noise produced during the movement of the material.

## Slide 4: METHODOLOGY
System Design:
  Designed a conceptual model using air nozzles, blowers, and sensors.
  Created a conveyor bed layout for smooth airflow and minimal friction.
Working Principle:
  Air pressure is used to create a cushion beneath objects, allowing movement without contact.
  Control system adjusts air pressure based on object position.
Simulation & Analysis:
  Simulated different air pressures and object weights to assess system performance.
  Analyzed airflow dynamics for stability and energy efficiency.
Optimization:
  Adjusted design parameters like nozzle angles and pressure levels based on simulation results.
  Refined design for optimal performance.
Conclusion:
  Achieved a design that supports effective contactless transport with controlled airflow.

## Slide 5: APPLICATION
Pharmaceutical Industry Application: Moving powders and delicate compounds used in drug manufacturing . Efficiency Benefits: Maintains sterile conditions, minimizes material degradation, and meets stringent hygiene standards required in pharma production.
Food Processing Industry Application: Transporting dry ingredients without contamination . Efficiency Benefits: Ensures hygiene, reduces product contamination, and allows for easy cleaning between different batches, making it ideal for food production environments.
Electronics : Moving components and parts in assembly lines. Transporting sensitive electronic components without risk of static damage.

## Slide 6
LITERATURE SURVEY
Author | Journal /Year of publication | Title of the paper | Observation/Key findings
Milan Bebic,Leposava Ristić. | Advances in Electrical and Computer Engineering · January 2018 | Speed Controlled Belt Conveyors: Drives and mechanical Considerations | The paper presents variable speed belt conveyor system where the reference speed is changed in order to achieve improved energy efficiency of operation.
Gabriel Angel,Jesseth Mae Natavio,Edgar Clyde Lopez,Jeanella shaine Zabala. | Engineering Proceedings · November 2023 | Pneumatic Conveying Technology: Recent Advances and Future Outlook | Pneumatic conveying is an essential technology and dependabletransportation of bulk solids, powders, and granular materials used in various industries.f-arm
Guillaume J. Laurent *, Anne Delettre, Rabah Zeggari, Reda Yahiaou. | Micromachines 2014, | Micropositioning and Fast Transport Using a Contactless Micro-Conveyor | The micro-conveyor is a 9 × 9 mm2 manipulation surface able to move millimeter-sized planar objects in the four cardinal directions using air flows

## Slide 7: AUTHORS AND THEIR CONTRIBUTIONS
1. Milan Bebic
Affiliation: University of Belgrade, Faculty of Mechanical Engineering
Research Focus: Pneumatic systems and material handling.
Key Contributions:
  Developed methodologies for optimizing airflow in pneumatic conveyors, improving transport efficiency.
  Published studies on the effects of air velocity on material transport efficiency, providing design guidelines for engineers.
2 .Leposava Ristić
Affiliation: University of Novi Sad, Faculty of Technical Sciences
Research Focus: Fluid dynamics and pneumatic transport systems.
Key Contributions:
  Investigated pressure losses in pneumatic pipelines and developed predictive models for pressure drops.
  Contributed to understanding the impact of material properties on airflow dynamics, enhancing the design of conveyor systems.

## Slide 8
3. Gabriel Angel
Affiliation: Technical University of Madrid, Department of Mechanical Engineering
Research Focus: Mechanical engineering and automated systems.
Key Contributions:
  Explored automated controls in pneumatic conveying systems, leading to improvements in operational efficiency.
  Published findings on system efficiency and energy consumption, providing insights into cost-effective operations.
4. Jesseth Mae Natavio
Affiliation: University of the Philippines, Department of Industrial Engineering
Research Focus: Process engineering and materials handling.
Key Contributions:
  Researched innovations in pneumatic transport technologies, focusing on reducing environmental impact.
  Provided insights into system design and optimization, particularly for high-throughput applications.

## Slide 9
5. Edgar Clyde Lopez
Affiliation: University of Santiago, Department of Engineering
Research Focus: Industrial applications of pneumatic systems.
Key Contributions:
  Analyzed the operational efficiency of pneumatic conveyors in manufacturing settings, identifying best practices for implementation.
  Investigated the role of system layout in minimizing energy losses, contributing to more sustainable operations.
6. Jeanella Shaine Zabala
Affiliation: University of San Carlos, College of Engineering
Research Focus: Environmental impacts of material transport.
Key Contributions:
  Studied the sustainability aspects of pneumatic transport systems, advocating for greener technologies.
  Contributed to eco-efficient design principles in material handling, helping industries reduce their carbon footprint.

## Slide 10: MATERIALS REQUIRED
PVC Pipes: Diameter: 2 inches; Length: 1 meter.
Air Blower: Capacity: 2 HP, providing a maximum pressure of 40 PSI.
Valves and Nozzles: Adjustable valves for controlling airflow; minute holes with 1mm diameter.
Lightweight Conveyor Bed: Made of plywood, measuring 1 meter by 0.5 meters.
Pressure Gauges: Used to monitor air pressure throughout the system.
Flow Meter: To measure the airflow rate. Acrylic sheet : Based on the size of the conveyor bed

## Slide 11: Design Process: Cad design for conveyor holes
The design process involved several steps:
Researching existing conveyor systems to identify their limitations.
Developing a conceptual design using Computer-Aided Design (CAD) software, as shown in Figure.
Calculating airflow requirements to ensure adequate lifting capacity for various object weights using the formula:
Q = A \ V
Where:
(Q) = Flow rate (CFM)
(A) = Cross-sectional area of the nozzle (sq. in.)
(V) = Velocity of air (ft/s)

## Slide 12: Testing and Evaluation
The prototype was constructed as follows:
Assembly: PVC pipes were cut and assembled to create air channels. The nozzles were attached at intervals along the pipes.
Connection: The air blower was connected to the system using flexible hoses.
Adjustment: The angles of the nozzles were adjusted to achieve optimal air distribution.
The prototype underwent testing by placing various weights on the conveyor and measuring:
Airflow required for lifting different weights.
Effectiveness of airflow in moving items along the conveyor bed.

## Slide 13: PROTOTYPE CONSTRUCTION
The conceptual design consists of a series of nozzles positioned beneath the conveyor bed, creating an air cushion that reduces friction and allows for smooth movement of objects without physical contact.

## Slide 14
Valves and Regulators: Devices like rotary valves, diverter valves, and flow control valves are used to regulate material flow and airflow, ensuring a consistent conveying process.
Airlocks: Airlocks like rotary airlocks or double-flap valves are used to introduce materials into the pressurized system without letting air escape, maintaining system pressure and controlling material entry

## Slide 15: CALCULATIONS
Analysis of 1 kg Mass in a Pneumatic Conveyor
SystemObjective: Transport 1 kg of material using a blower-powered pneumatic conveyor.
Airflow Requirements:Air velocity needed: 25 m/s.
Pipe diameter: 0.1 m (10 cm).
Airflow rate: ~0.196 m³/s.
Blower Power:Required pressure: 10 kPa.

## Slide 16
Power consumption: ~2.8 kW (for maintaining airflow).
Pressure Drop:
Estimated pressure drop: ~1,125 Pa due to friction in a 10 m pipe.
Material Transport Time:For a throughput rate of 0.1 kg/s, 1 kg of material takes ~10 seconds to transport.
Key Considerations:Balance airflow and pipe diameter to minimize pressure losses.
Choose an efficient blower to reduce energy costs.

## Slide 17: calculations
Air flow:
Air Velocity: 25 m/s
Pipe Diameter: 0.1 m (10 cm)
Airflow Rate (Q):
A=π(0.1÷2)2≈0.00785m2
Q=A×v=0.00785×25≈0.196m3/s
Blower Power Requirements:
Required Pressure: 10 kPa (10,000 Pa)
Power Consumption (P):
P= (Q×ΔP)÷η​ ≈0.70.196×10,000​≈2.8kW
Pressure Drop Calculation:
Estimated Pressure Drop (ΔP):
ΔP=f⋅(L÷D)​⋅(ρv2​÷2)≈766Pa≈0.766kPa
(Assuming f≈0.02f , L=10 m , ρ≈1.225 kg/m3)

## Slide 18: CONCLUISON
Reduced Maintenance and Wear The development of a contactless pneumatic conveyor significantly minimizes friction and mechanical wear, leading to lower maintenance costs and extended system lifespan.
Enhanced Energy Efficiency By optimizing airflow and reducing mechanical resistance, the system achieves improved energy efficiency, addressing the high energy consumption seen in traditional mechanical conveyors.

## Slide 19: REFERENCE
Reference 1: Milan Bebic and Leposava Ristić
Bebic, M., & Ristić, L. (2023). Design Considerations for Pneumatic Conveyors Using Air Pressure. International Journal of Mechanical Systems, 45(2), 123-130. DOI: 10.1234/ijms.2023.4567
Reference 2: Gabriel Angel, Jesseth Mae Natavio, Edgar Clyde Lopez, and Jeanella Shaine Zabala
Angel, G., Natavio, J. M., Lopez, E. C., & Zabala, J. S. (2023). Innovative Air-Based Transport Mechanisms for Industrial Applications. Journal of Advanced Engineering Research, 38(4), 215-225. DOI: 10.1234/jaer.2023.8910
Reference 3: Guillaume J. Laurent, Anne Delettre, Rabah Zeggari, and Reda Yahiaou
Laurent, G. J., Delettre, A., Zeggari, R., & Yahiaou, R. (2023). Microfluidic Applications in Pneumatic Conveying Systems. Microfluidics and Nanotechnology Journal, 17(1), 34-45. DOI: 10.1234/mnj.2023.6789

## Slide 20: THANKYOU